## Slide 1: MODEL FOR ‘COMPENSATION IN ENERGY’ IN CASE OF CURTAILMENT OF GENERATION ON DSO GRID
CWAPE
GT GFLEX 2
1.10.2014

## Slide 2: ESTIMATON VOLUMES REFERENCE PROFILE
Nominations
Historical data
Distinction between controllable (e.g. biomass, cogeneration, gas motor, …) and limited controllable (e.g. wind turbines) units
Nominations are the most accurate estimations by a BRP
Basic principle
Free choice of generator between ‘nominations’ and ‘reference profile based on historical data’
DSO needs a reference profile to determine the activated volume (= non-generated energy) for counter-balancing and settlement
Nominations ensure coherence between markets and enhance the flexibility market (respect of the flexibility value chain)
Nominations allow trade-off for use of flexibility in different markets, e.g. nominations are already used to valorise flexibility in the balancing market (e.g. cogeneration unit supplying R2)
Controllable units: reference profile based on historical data of specific unit
Limited controllable units: reference profile based on historical data in a geographical area, e.g. country, region, province, … (= proposal Elia)

## Slide 3: BALANCE OF SYSTEM IS KEY
FEBEG congestion management model is based on neutralizing impact on balancing market (‘redispatch’)
Inspired by Elia congestion rules in ‘CIPU’:
  Outcome of learning curve
  EU supported system
  Respects the BRP-balancing obligation
Main goal: system balance is not influenced by congestion management on DSO level

## Slide 4: GENERAL PROCESS
Distribution Grid User
DSO
TSO Compen-sation Tool
BRP
Retailer
DSO
FSP
BSP
Congestion bids = compensation bids
- 3 MW
- 3 MW
- 3 MW
+ 3 MW
+ 3 MW
BRP is balanced!
- 3 MW
- 3 MW

## Slide 5: CONGESTION BIDS = COMPENSATIONS BIDS
Congestion bids: DSO adapts generation (= curtailment) to deal with system constraints
    Connection agreement: technical flexibility imposed in the connection agreement between GU and DSO
    Commercial agreement: flexibility services offered on a voluntary basis to a DSO, e.g. generation down by GU with firm capacity or consumption up
  Compensation bids: DSO activates a compensation bid on the TSO Compensation Tool in order to compensate for the impact of the curtailment
Transfer of energy via automatic correction of BRP perimeter via TSO on request of DSO.

## Slide 6: OBLIGATORY CONGESTION BID
Distribution Grid User
DSO
TSO Counter-balancing
BRP
Retailer
DSO
FSP
BSP
- 3 MW
- 3 MW
+ 3 MW
+ 3 MW
    Technical flexibility is imposed in the connection agreement between GU and DSO
    GU is obliged to make a congestion bid to the DSO according to the specific requirements in the connection agreement with regard to the technical flexibility, i.e. curtailment of generation
    DSO decision to activate or not
- 3 MW

## Slide 7: VOLUNTARY CONGESTION BID
Distribution Grid User
DSO
TSO Compen-sation Tool
BRP
Retailer
DSO
FSP
BSP
- 3 MW
- 3 MW
+ 3 MW
+ 3 MW
    GU becomes a FSP or signs a flexibility services agreement with a FSP
    FSP makes a voluntary congestion bid to the DSO, i.e. curtailment of generation or increase of consumption
    DSO decision to activate or not the congestion bid
- 3 MW
- 3 MW

## Slide 8: FINANCIAL FLOWS
Distribution Grid User
DSO
TSO Compen-sation Tool
BRP
Retailer
DSO
FSP
BSP
- 3 MW
- 3 MW
+ 3 MW
+ 3 MW
    Curtailed volume is generated by other generator or compensated by load shedding
    Grid user will be paid by retailer/BRP for production as if no activation was done
    GU/FSP pays variable running costs to DSO (fuel cost, CO2 costs, maintenance, … - green certificate)
    DSO pays TSO for compensation bid
- 3 MW
Contractual settlement as if no activation was done
Contractual settlement as if no activation was done
DSO pays for compensation bid
GU/FSP pays DSO for congestion bid
- 3 MW
- 3 MW

## Slide 9: COMPENSATION BIDS
Only TSO can compensate perimeter BRP
Need of cooperation between DSO and TSO
TSO Compensation Tool:
  To maximise liquidity, at least following means should be available via TSO Compensation Tool:
    Bidladder: compensation bids should have a locational signal
      Skip bids to avoid congestion
      Select specific bids to compensate locally
    CIPU: compensation bids by units connected to the transmission grid
  Remuneration of compensation bid will generally be cheaper than imbalance price (imbalance price is cap)

## Slide 10: ADVANTAGES
No impact on commodity/balancing market (perimeter BRP)
Proposal integrates existing tools or tools under development, e.g. know-how of bidladder
Proposal could strengthen - if future integration of redispatch tool in bidladder - the balancing market creating liquidity
Proprosal looks for most cost-efficient solution:
  Most favorable congestion bid (merit order)
  Cheapest compensation bid in whole system (merit order)
  DGO cost is limited to difference between both (net cost is incentive to invest)
Extendable to other cases, e.g. generation up, load down and up
Neutral for BRP, retailer and grid user
Level playing field between grid users

## Slide 11: QUESTIONS

## Slide 12: CONTACT
Vincent Debloca
vincent.deblocq@febeg.be
0032-2 500 85 94
www.febeg.be